## Slide 1: Spill Response Termination
Notes: Welcome / title slide. Introduce Module 10, which covers how to properly close out and terminate a spill response - deciding when to stop, standing down resources, and the follow-up work (debriefs, reporting, post-spill studies) that comes after field operations end.

## Slide 2
Spill Response Termination
Objectives
To list what the tasks that must be completed at the end of a spill
1
How to determine when to demobilise
2
Understand the steps involved in the development of post spill studies
3
Notes: Set out the three objectives for this module:
1. Understand the tasks that must be completed at the end of a spill.
2. Understand how to determine when to demobilise.
3. Understand the steps involved in the development of post-spill studies.

## Slide 3: What are the steps to terminating a spill response?
Notes: Terminating an oil spill response involves several key steps to ensure that all aspects of the response are properly concluded and documented. Here’s a list of the steps typically involved in this process:
1. Assessment of Clean-Up Objectives:
- Evaluate whether the cleanup objectives have been met according to pre-defined environmental and operational criteria.
2. Final Monitoring and Evaluation:
- Conduct comprehensive environmental monitoring to assess the recovery of the affected areas.
- Perform SCAT (Shoreline Cleanup Assessment Technique) surveys if applicable, to ensure no further recoverable oil remains.
3. Demobilization of Resources:
- Organize the systematic withdrawal of personnel and equipment from the site.
- Clean, repair, and return equipment to storage or rental agencies.
4. Debriefing and Reporting:
- Hold debrief sessions with all teams to discuss the response actions, challenges faced, and lessons learned.
- Prepare a final report that documents the response actions, effectiveness, and any follow-up actions required.
5. Incident Closure:
- Officially declare the end of the incident response phase.
- Notify all stakeholders, including local communities, government bodies, and media, if appropriate, about the end of response activities.
6. Post-Incident Review:
- Conduct a thorough review of the entire incident response to identify successes and areas for improvement.
- Update response plans and training programs based on lessons learned during the incident.
7. Continued Monitoring:
- Implement a plan for ongoing monitoring of the environment to detect any long-term impacts from the spill.
- Ensure continued engagement with local communities and stakeholders to address any residual concerns.
8. Restoration and Recovery Programs:
- If necessary, initiate longer-term ecological restoration projects to fully restore any remaining environmental damage.
- Monitor and support these restoration efforts until ecosystem recovery is confirmed.
9. Financial and Legal Closure:
- Finalize all financial accounting for the response, including cost recovery from responsible parties.
- Complete any necessary legal documentation or proceedings related to the spill.
These steps help ensure that the termination of an oil spill response is as comprehensive and effective as the initial response, aiming for full recovery and minimizing long-term environmental impacts.

## Slide 4
Assessment of Clean-Up Objectives
Terminating a Response
Final Monitoring and Evaluation
Demobilization of Resources
Evaluate whether the cleanup objectives have been met according to pre-defined environmental and operational criteria.
Conduct comprehensive environmental monitoring to assess the recovery of the affected areas.
Perform SCAT (Shoreline Cleanup Assessment Technique) surveys if applicable, to ensure no further recoverable oil remains.
Organize the systematic withdrawal of personnel and equipment from the site.
Clean, repair, and return equipment to storage or rental agencies.
Notes: Trainer note: this slide's notes previously repeated the full 9-step list used on slide 3 - trimmed here to the three steps actually shown on this slide.
Assessment of Clean-Up Objectives: evaluate whether the cleanup objectives have been met against pre-defined environmental and operational criteria.
Final Monitoring and Evaluation: conduct comprehensive environmental monitoring to assess recovery of the affected areas, and perform SCAT surveys where applicable to confirm no further recoverable oil remains.
Demobilization of Resources: organise the systematic withdrawal of personnel and equipment from site, and clean, repair and return equipment to storage or rental agencies.

## Slide 5
Debriefing and Reporting
Terminating a Response
Incident Closure
Post-Incident Review
Hold debrief sessions with all teams to discuss the response actions, challenges faced, and lessons learned.
Prepare a final report that documents the response actions, effectiveness, and any follow-up actions required.
Officially declare the end of the incident response phase.
Notify all stakeholders, including local communities, government bodies, and media, if appropriate, about the end of response activities.
Finalize all financial accounting for the response, including cost recovery from responsible parties.
Complete any necessary legal documentation or proceedings related to the spill.
Notes: Trainer note: this slide's notes previously repeated the full 9-step list used on slide 3 - trimmed here to the three steps actually shown on this slide.
Debriefing and Reporting: hold debrief sessions with all teams to discuss response actions, challenges and lessons learned, and prepare a final report documenting response actions, effectiveness and any follow-up required.
Incident Closure: officially declare the end of the incident response phase and notify stakeholders (local communities, government bodies, media where appropriate) that response activities have ended.
Post-Incident Review: conduct a thorough review of the whole response to identify successes and areas for improvement, and update response plans and training based on lessons learned.

## Slide 6
Continued Monitoring
Terminating a Response
Restoration and Recovery Programs
Financial and Legal Closure
Implement a plan for ongoing monitoring of the environment to detect any long-term impacts from the spill.
Ensure continued engagement with local communities and stakeholders to address any residual concerns.
If necessary, initiate longer-term ecological restoration projects to fully restore any remaining environmental damage.
Monitor and support these restoration efforts until ecosystem recovery is confirmed.
Conduct a thorough review of the entire incident response to identify successes and areas for improvement.
Update response plans and training programs based on lessons learned during the incident.
Notes: Trainer note: this slide's notes previously repeated the full 9-step list used on slide 3 - trimmed here to the three steps actually shown on this slide.
Restoration and Recovery Programs: where necessary, initiate longer-term ecological restoration projects and monitor/support them until ecosystem recovery is confirmed.
Continued Monitoring: implement a plan for ongoing environmental monitoring to detect any long-term impacts, and keep engaging local communities and stakeholders on residual concerns.
Financial and Legal Closure: finalise all financial accounting, including cost recovery from responsible parties, and complete any outstanding legal documentation or proceedings.

## Slide 7: When should we terminate?
Notes: Section divider. Transitions from 'what are the steps to terminate a response' into the harder question of 'when' - the decision criteria for calling an end to the response, covered on the next slide.

## Slide 8
When should we terminate?
Objectives Achieved: Terminate when clean-up objectives are met.
No Further Recoverable Oil: End efforts if remaining oil cannot be effectively recovered.
Environmental Recovery: Conclude response once affected areas meet environmental recovery criteria.
Stakeholder Consensus: Ensure agreement among stakeholders that the response has been sufficient.
Resource Optimization: Demobilize when resources and personnel are no longer efficiently used.
Regulatory Approval: Finish only after meeting all regulatory requirements and obtaining official closure.
Safety Considerations: Stop if continuing poses safety risks with minimal environmental or recovery benefits.
Economic Justification: Evaluate if further clean-up costs are justified by the expected environmental benefits.
Notes: Walk through the criteria used to decide when to terminate a response - objectives achieved, no further recoverable oil, environmental recovery criteria met, stakeholder consensus, resources no longer efficiently used, regulatory approval obtained, safety risks outweighing remaining benefit, and whether further clean-up cost is still justified by the environmental benefit gained.
Useful discussion point: in practice this is rarely a single trigger - it's a judgement call weighing several of these criteria together, and stakeholder/regulatory agreement is often the final gate even once the technical criteria are met.

## Slide 9
Field Operations
Terminating a Response
Disassemble Equipment: Take apart the equipment used during the response.
Organize Parts: Keep all component parts grouped together.
Clean Equipment: Thoroughly clean all equipment before it's moved.
Transport Equipment: Safely transport equipment back to storage or other locations.
Prevent Contamination: Implement measures to prevent any secondary contamination during these processes.
Incident Management Functions
Phase Out and Transfer Command: Gradually reduce operations and transfer command following the organizational chart.
Ensure Support for Field Operations: Continue providing necessary support to field activities.
Monitor and Document Actions: Consistently track and document all actions and costs.
Compile Logs and Incident Data: Gather all logs and incident-related information from participants.
Notify Authorities: Inform all relevant local and national government authorities and nearby operators.
Maintain Role Oversight: Keep a clear overview of all functional roles during the scale-back process.
Notes: Trainer note: this slide's notes previously carried the full 9-step list from slide 3, which doesn't match this slide's content - replaced below with notes on Field Operations and Incident Management Functions.
Field Operations (physical stand-down): disassemble equipment, keep component parts organised together, clean equipment thoroughly before it's moved, transport it safely back to storage, and take measures to prevent secondary contamination throughout.
Incident Management Functions (organisational stand-down): phase out and transfer command following the org chart, continue supporting field operations while this happens, keep monitoring and documenting actions and costs, compile logs and incident data from all participants, notify relevant local and national authorities and nearby operators, and maintain oversight of all functional roles throughout the scale-back.

## Slide 10: Decontamination Facilities
What needs to be considered for the recovery and decontamination of equipment?
Notes: For an effective Decontamination facility the risks that have to be considered are:
  Area in general under adequate control
  H & S of Personnel and their cleanliness
  Water supply to the facility
  Drainage both natural and installed
  Wash down facility leaves no residual traces
  Disposal of solid and liquid waste generated

## Slide 11: How would you structure a Debrief?
List the areas you would cover
Who should be present
When should it be held?
Notes: Structuring a debrief after an oil spill response is crucial for learning and improving future responses. Here’s how you could structure it:
Areas to Cover:
1. Incident Overview: Recap the incident's specifics, including the size, location, and type of oil spilled.
2. Response Actions: Discuss what actions were taken during the response, including initial reaction, containment, and cleanup efforts.
3. Effectiveness of Response: Evaluate the effectiveness of the response strategies and tactics used.
4. Communication and Coordination: Review the communication flow both internally among the response team and externally with the public, media, and other stakeholders.
5. Resource Management: Assess how resources were managed and deployed, including personnel, equipment, and financial resources.
6. Safety Issues: Discuss any safety incidents or concerns that arose during the response.
7. Environmental Impact: Evaluate the environmental impact of the spill and the efficacy of mitigation efforts.
8. Compliance and Legal Issues: Review any compliance or legal issues encountered.
9. Lessons Learned: Identify what was learned and what could be improved for future responses.
10. Recommendations for Future Responses: Compile recommendations based on the debriefing discussions.
Who Should Be Present:
- Response Team Leaders: Incident commanders and section chiefs from various response teams (e.g., operations, planning, logistics).
- Field Workers: Representatives from on-ground teams who can provide insights into field operations.
- Environmental Experts: Specialists who can speak to the environmental impact and recovery.
- Government Representatives: Officials from relevant regulatory agencies who were involved in the response.
- External Partners: Representatives from non-governmental organizations, industry partners, and other stakeholders.
- Health and Safety Officers: To address safety performance and concerns during the incident.
- Legal Advisors: To provide insights on compliance and legal implications.
When Should It Be Held:
- Timing: The debrief should be held soon after the response has concluded to ensure that the details of the incident are fresh in everyone's minds. Ideally, this should be within a few weeks of the termination of field operations.
- Follow-Up: Consider scheduling a follow-up meeting after the initial debrief to review the implementation of improvements and changes based on the lessons learned.
This structured approach ensures that all aspects of the response are analyzed thoroughly, leading to tangible improvements in future spill response efforts.

## Slide 12: Recap
List three things you have learnt from this session
Notes: Trainer note: this slide's notes previously referenced SCAT, which belongs to a different module - replaced below with notes for this recap slide.
Closing recap exercise: ask delegates to individually note down three things they've learnt from this module (e.g. the steps to terminate a response, the criteria for deciding when to demobilise, or what a good debrief/post-spill study covers), then share with the group. Use their answers to check understanding and address any gaps before closing.