## Slide 1
The purpose of this exercise is to test your knowledge of responding to an oil spill
Notes: https://map.openseamap.org/
Welcome the group and explain that this exercise tests their knowledge of selecting an appropriate oil spill response strategy.
Starter Activity (10 minutes), step 1: introduce the objectives, then have participants scan the QR code to locate the exercise area (see map link below).

## Slide 2
Exercise 1: Identify the Sensitivities
Location: Isle of Portland, UK
Notes: Red Line is County border - added for presentation purposes only to encourage thoughts of contacting neighbouring county
Location: Isle of Portland, UK. Have participants scan the QR code / locate the area on the map shown.
Form groups (Starter Activity step 2): divide participants into groups of 4-5. Assign each group one category of sensitivities to research - Environmental, Economic, or Sociological.

## Slide 3
Isle of Purbeck Sensitivities
Environmental | Economic | Sociological
Marine mammals | Commercial Harbour | Recreational Sailing
Shoreline birds | Tourism | Watersports
SSI’s | Stone Quarrying | Hiking
UNESCO | Prison | Fishing
Notes: Starter Activity step 3: each group feeds back the sensitivities they identified to the wider group so everyone becomes familiar with the area.
Use this table as a starting reference - Environmental (marine mammals, shoreline birds, SSSIs, UNESCO site), Economic (commercial harbour, tourism, stone quarrying, prison), Sociological (recreational sailing, watersports, hiking, fishing).
Encourage groups to add anything relevant they found that isn't listed here.

## Slide 4
From the scenarios given, decide on the appropriate response strategy in each case.
Monitor and evaluate
Dispersants
Containment and Recovery
Protection
Shoreline clean-up (or others)
Notes: Main Activity begins (25 minutes). Explain that 6 scenarios will be shown in turn.
For each scenario, give groups 10 minutes to discuss and agree which response strategy they would use and why, choosing from: Monitor and evaluate, Dispersants, Containment and Recovery, Protection, Shoreline clean-up (or others).
Remind groups to justify their choice using the weather conditions, oil type, and spill movement shown on each scenario map.

## Slide 5
Wind Speed | 20 knots
Wave Height | 2 mtr
Visibility | Good
Oil | HFO
Quantity | 100 tonnes
Scenario 1
10:00
16:00
Notes: Scenario 1: HFO spill of 100 tonnes, tracked from 10:00 to 16:00, in 20 knot winds, 2m waves, and good visibility.
Give groups 10 minutes to decide on their response strategy and reasoning. HFO is a heavy, persistent oil - prompt groups to consider how that affects their choice.

## Slide 6
Wind Speed | 20 knots
Wave Height | 2 mtr
Visibility | Good
Oil | HFO
Quantity | 100 tonnes
10:00
16:00
Scenario 1
Notes: Facilitate group feedback on Scenario 1. Ask each group to share their chosen response strategy and reasoning.
Compare the different approaches across groups, then discuss what they would do differently and which aspects of a real response would be most effective here.

## Slide 7
Wind Speed | 6 knots
Wave Height | 0.2 mtr
Visibility | Good
Oil | IFO
Quantity | 100 tonnes
Scenario 2
04:00
12:00
Notes: Scenario 2: IFO spill of 100 tonnes, tracked from 04:00 to 12:00, in a lighter 6 knot wind, 0.2m waves, and good visibility.
Give groups 10 minutes to decide on their response strategy and reasoning, taking into account the calmer conditions compared with Scenario 1.

## Slide 8
Wind Speed | 6 knots
Wave Height | 0.2 mtr
Visibility | Good
Oil | IFO
Quantity | 100 tonnes
04:00
12:00
Scenario 2
Notes: Facilitate group feedback on Scenario 2. Ask each group to share their chosen response strategy and reasoning.
Compare approaches across groups and discuss what they would do differently, and how the calmer weather here changes the response compared with Scenario 1.

## Slide 9
Wind Speed | 8 knots
Wave Height | 0.5 mtr
Visibility | Good
Oil | Condensate
Quantity | 500 tonnes
08:00
18:00
Scenario 3
Notes: Scenario 3: Condensate spill of 500 tonnes - a much larger quantity - tracked from 18:00 to 08:00 overnight, in 8 knot winds, 0.5m waves, and good visibility.
Give groups 10 minutes to decide on their response strategy and reasoning. Condensate is light and volatile - prompt groups to consider evaporation and natural dispersion alongside the larger spill volume.

## Slide 10
Wind Speed | 8 knots
Wave Height | 0.5 mtr
Visibility | Good
Oil | Condensate
Quantity | 500 tonnes
08:00
18:00
Scenario 3
Notes: Facilitate group feedback on Scenario 3. Ask each group to share their chosen response strategy and reasoning.
Compare approaches across groups and discuss what they would do differently, particularly given the larger quantity involved.

## Slide 11
Wind Speed | 10 knots
Wave Height | 0.5 mtr
Visibility | Good
Oil | Gas Oil
Quantity | 15 tonnes
Scenario 4
09:00
12:00
18:00
Notes: Scenario 4: Gas Oil spill of 15 tonnes - the smallest quantity in the exercise - tracked across 09:00, 12:00 and 18:00, in 10 knot winds, 0.5m waves, and good visibility.
Give groups 10 minutes to decide on their response strategy and reasoning, considering whether a smaller, lighter-oil spill changes their approach.

## Slide 12
Wind Speed | 10 knots
Wave Height | 0.5 mtr
Visibility | Good
Oil | Gas Oil
Quantity | 15 tonnes
09:00
12:00
18:00
Scenario 4
Notes: Facilitate group feedback on Scenario 4. Ask each group to share their chosen response strategy and reasoning.
Compare approaches across groups and discuss what they would do differently.

## Slide 13
12:00
21:00
Wind Speed | 8 knots
Wave Height | 0.4 mtr
Visibility | Good
Oil | Emulsified
Quantity | 100 tonnes
Scenario 5
Notes: Scenario 5: Emulsified oil spill of 100 tonnes, tracked from 12:00 to 21:00, in 8 knot winds, 0.4m waves, and good visibility.
Give groups 10 minutes to decide on their response strategy and reasoning. Emulsified oil is thicker and more persistent - prompt groups to discuss how this affects recovery options.

## Slide 14
Wind Speed | 8 knots
Wave Height | 0.4 mtr
Visibility | Good
Oil | Emulsified
Quantity | 100 tonnes
12:00
21:00
Scenario 5
Notes: Facilitate group feedback on Scenario 5. Ask each group to share their chosen response strategy and reasoning.
Compare approaches across groups and discuss what they would do differently.

## Slide 15
Wind Speed | 20 knots
Wave Height | 2 mtr
Visibility | Good
Oil | Brent Blend
Quantity | 100 tonnes
Scenario 6
07:30
04:00
Notes: Scenario 6: Brent Blend spill of 100 tonnes, tracked from 04:00 to 07:30, in 20 knot winds, 2m waves, and good visibility - the roughest conditions in the exercise.
Give groups 10 minutes to decide on their response strategy and reasoning, considering how the stronger wind and wave conditions affect the options available.

## Slide 16
Wind Speed | 20 knots
Wave Height | 2 mtr
Visibility | Good
Oil | Brent Blend
Quantity | 100 tonnes
07:30
04:00
Scenario 6
Notes: Facilitate group feedback on Scenario 6. Ask each group to share their chosen response strategy and reasoning.
Compare approaches across groups and discuss what they would do differently.
End Activity (5 minutes): request feedback from participants on the exercise itself, and discuss what insights they've gained and how these can be applied to real-world incident management.