## Slide 1: Shoreline Assessment
Notes: Introduce the shoreline assessment module and explain its importance within oil spill response operations.

## Slide 2: Shoreline Assessment
Understand the phases and principles of shoreline assessment
1
2
3
Understand the logistical requirements to conduct shoreline assessment
Consider what equipment they should use to carry out the assessment and evaluation
Objectives
Notes: Review the learning objectives and explain what participants should be able to do by the end of the session.

## Slide 3: Shoreline Assessment
Why do we need it?
Notes: Ask participants why shoreline assessment is necessary and how assessment data supports response decisions.

## Slide 4: 3 Phases of a SCAT Program
Reconnaissance Survey
“ground-truthing” (detailed info)
“sign-off” process
Initial Phase
Ground SCAT
Post-treatment surveys
Notes: Explain the three phases of a SCAT program: reconnaissance, detailed ground surveys and post-treatment sign-off.

## Slide 5: Shoreline Clean-up Assessment Technique
Can be used Pre-spill or During spill to survey the affected area
Collecting data aids the decision making process
“Eyes and ears of Planning and Operations”
Notes: Introduce SCAT as a structured process that provides information for planning and operational decision making.

## Slide 6: 5 Principles of SCAT
Systematic survey
Shoreline division into segments
Standardised terms and definitions
Team of inter-agency personnel
Management and operational support:
Operational priorities
Treatment guidelines
End point criteria
Sign off process
A
Notes: Review the five key SCAT principles including standardisation, segmentation and clear endpoint criteria.
The 5 key SCAT (Shoreline Cleanup Assessment Technique) principles from your training material are: [Module 6 -...Assessment | PowerPoint]
Systematic Survey
  Conduct shoreline assessments using a consistent, organized approach.
  Ensures the entire affected area is evaluated and documented. [Module 6 -...Assessment | PowerPoint]
Shoreline Division into Segments
  Divide the shoreline into manageable segments with unique identifiers.
  Makes assessment, reporting, and cleanup planning more effective. [Module 6 -...Assessment | PowerPoint]
Standardised Terms and Definitions
  Use agreed terminology for shoreline types, oiling conditions, and treatment recommendations.
  Ensures consistency between teams and over the duration of the response. [Module 6 -...Assessment | PowerPoint]
Interagency Team Approach
  SCAT assessments are carried out by representatives from multiple agencies and stakeholders.
  Brings together environmental, operational, regulatory, scientific, and local knowledge. [Module 6 -...Assessment | PowerPoint]
Management and Operational Support
  Assessment data is used to support:
    Operational priorities
    Treatment recommendations/guidelines
    Cleanup endpoints
    Sign-off decisions
  SCAT acts as the link between field observations and response management decisions. [Module 6 -...Assessment | PowerPoint]
A simple way to remember them is:
Survey → Segment → Standardise → Stakeholders → Support Decisions.

## Slide 7: Inter Agency Personnel
Who should be involved in a SCAT team?
Notes: Discuss the organisations and specialists typically represented in an interagency SCAT team.

## Slide 8: Inter Agency Personnel
Can be used Pre-spill or During spill to survey the affected area
Collecting data aids the decision making process
“Eyes and ears of Planning and Operations”
Notes: Reinforce that SCAT teams act as the eyes and ears of planning and operations by collecting reliable field data.

## Slide 9: Assigned unique location code e.g. EI-1
Units for consistent recording and comparison throughout spill
Typical range 0.2 to 2km (200-2000m)
Similar physical features and sediment type within each segment
Boundaries –
Prominent geological features
1
Changes in shoreline or substrate type
2
Change in oiling conditions
3
Operational area/access
4
Eagle Island
Notes: Explain shoreline segmentation, the use of unique identifiers and the importance of consistent boundaries.
Shoreline segmentation is the process of dividing a shoreline into manageable sections (segments) that have similar physical, environmental, and operational characteristics. It is a fundamental component of the SCAT process because it allows assessment teams to describe conditions consistently, prioritize response actions, and track cleanup progress. [Module 6 -...Assessment | PowerPoint]
Why do we segment shorelines?
Provides a consistent framework for assessment and reporting. [Module 6 -...Assessment | PowerPoint]
Makes it easier to identify and map oiling conditions. [Module 6 -...Assessment | PowerPoint]
Supports operational planning and resource allocation. [Module 6 -...Assessment | PowerPoint]
Enables progress tracking and cleanup sign-off for specific areas. [Module 6 -...Assessment | PowerPoint]
Segment Characteristics
According to your training material, shoreline segments should:
Be assigned a unique location code (e.g., EI-1 for Eagle Island Segment 1). [Module 6 -...Assessment | PowerPoint]
Typically range from 200 m to 2 km in length. [Module 6 -...Assessment | PowerPoint]
Contain similar shoreline type, substrate, and physical features throughout the segment. [Module 6 -...Assessment | PowerPoint]
Be suitable units for consistent recording and comparison during a spill response. [Module 6 -...Assessment | PowerPoint]
Common Segment Boundaries
Segment boundaries are usually established where there is a:
Prominent geological feature (headland, river mouth, cliff). [Module 6 -...Assessment | PowerPoint]
Change in shoreline or substrate type (sand to rock, mud to gravel). [Module 6 -...Assessment | PowerPoint]
Change in oiling conditions. [Module 6 -...Assessment | PowerPoint]
Change in operational area or access. [Module 6 -...Assessment | PowerPoint]
Levels of Segmentation
Simple Segmentation
Based primarily on shoreline type.
Usually sufficient for pre-spill planning and mapping.
Requires less effort and fewer rules. [Module 6 -...Assessment | PowerPoint]
Detailed Segmentation
Considers projected oil behaviour, access, exposure, and cleanup requirements.
May subdivide existing segments into smaller operational units.
Common during an active spill response.

## Slide 10: How would you split up this shoreline?
Notes: Facilitate discussion on how participants would divide the shoreline into logical assessment segments.

## Slide 11
AB-2
AB-4
AB-3
AB-1
PRIMARY = Shore type only
SIMPLE SEGMENTATION
This is the basics – good enough for most pre-SCAT mapping purposes
Notes: Explain simple segmentation based mainly on shoreline type and physical characteristics.

## Slide 12
AB-3
AB-4
AB-5
AB-7
AB-1
AB-2
AB-6
Based on projected oil behavior
MORE DETAILED SEGMENTATION
Optional – will come later if/when needed
Requires more effort and more rules
SECONDARY could subdivide on backshore and/or potential oil behavior
Increases from 4 to 7 segments
Notes: Explain more detailed segmentation that considers oil behaviour, access and operational requirements.

## Slide 13: Task - Pre Segment
You have been tasked to segment the local shoreline (peace time – no oil present)
1
2
You can use Google Earth and other resources to pre segment the shoreline
Click to edit Master text styles
Notes: Introduce the exercise and explain how participants can use mapping tools to pre-segment a shoreline.
For a pre-spill shoreline segmentation exercise, participants can use mapping tools such as Google Earth, ArcGIS, QGIS, nautical charts, aerial photographs, and local shoreline maps to divide the coastline into logical SCAT segments before an incident occurs. [Module 6 -...Assessment | PowerPoint]
Step 1: Review the Shoreline
Examine the shoreline using satellite imagery and identify:
Sandy beaches
Rocky shorelines
Gravel/cobble beaches
Mudflats
Marshes and wetlands
Man-made structures such as seawalls, jetties, and ports
Each shoreline type will behave differently if oil reaches it. [Module 6 -...Assessment | PowerPoint]
Step 2: Identify Natural Boundaries
Create segment boundaries where there are clear physical changes such as:
Headlands
River mouths
Cliffs
Changes in substrate type
Harbour entrances
Access points
These features provide logical and repeatable segment limits. [Module 6 -...Assessment | PowerPoint]
Step 3: Consider Operational Factors
Look beyond physical features and consider:
Vehicle access
Boat access
Public access restrictions
Sensitive environmental areas
Potential staging locations
A shoreline section that requires different operational resources may need to be a separate segment. [Module 6 -...Assessment | PowerPoint]
Step 4: Create Segment Codes
Assign each segment a unique identifier, for example:
BR-01
BR-02
BR-03
or
EI-1
EI-2
EI-3
These codes are used throughout assessment, planning, cleanup operations, and final sign-off. [Module 6 -...Assessment | PowerPoint]
Step 5: Check Segment Length
SCAT segments are typically:
200 m to 2 km long
Consistent in shoreline type and characteristics
Large enough to manage efficiently but small enough to describe accurately [Module 6 -...Assessment | PowerPoint]
Step 6: Produce a Segment Map
Participants should create a map showing:
Segment boundaries
Segment IDs
Shoreline type
Access locations
Sensitive resources
Potential operational constraints

## Slide 14: Shoreline Survey Form
Notes: Introduce the shoreline survey form and explain its purpose in capturing standardised field observations.

## Slide 15: Your Shoreline Oiled Summary Form
Notes: Discuss shoreline oiled summary forms, consistency of terminology and the importance of team agreement.
"The Shoreline Oiled Summary Form is fundamental to the SCAT process. It provides a consistent way of recording observations and communicating information to Operations and Planning. While forms can be adapted to suit different spill environments, consistency is critical. If one team calls something a tar ball, every team must use that same definition. SCAT assessments should be completed collaboratively, with the team agreeing on oiling descriptions, treatment recommendations, and cleanup endpoints before the form is finalized."

## Slide 16
Notes: Review the example form and highlight key sections that require accurate field observations.

## Slide 17
Notes: Continue reviewing the form and explain how observations should be recorded consistently.

## Slide 18
Notes: Explain any remaining parts of the form and answer questions before moving to oiling assessment.

## Slide 19: Section 6 – Surface oiling
Most important part of the process
Quantitative measurement of oiling
Standard terminology
No oil, then record
Zone the shoreline for accurate recording
Zones start with “A” as lowest on shore
One zone (designated A) if segment oiling is uniform along/across shore
As many zones as necessary for an accurate description
Notes: Discuss surface oiling assessment, zoning and the use of standard terminology for quantitative descriptions.

## Slide 20: Tidal zones
SU
UI
MI
LI
High Tide line
SU - Supratidal
UI – Upper Intertidal
MI – Mid Intertidal
LI – Lower intertidal
Notes: "Dividing the shoreline into tidal zones is essential for accurate oiling assessment. The Supratidal, Upper Intertidal, Mid Intertidal, and Lower Intertidal zones experience different levels of tidal influence, which affects how oil is deposited, transported, and naturally removed. By recording oiling conditions separately within each zone, SCAT teams can provide more accurate assessments and develop more effective cleanup recommendations.
Tidal Zones and Their Importance in SCAT
When conducting a shoreline assessment, the shoreline is divided into tidal zones to accurately describe where oil is located. This helps responders understand the potential movement of oil, select appropriate cleanup methods, and monitor natural recovery. [Module 6 -...Assessment | PowerPoint]
1. Supratidal Zone (SU)
Located above the normal high tide line.
Only affected by extreme high tides, storm surges, or wave splash.
Oil found here can persist for long periods because it is not regularly washed by tides. [Module 6 -...Assessment | PowerPoint]
Significance:
Often requires active cleanup.
May contain heavily weathered oil deposits.
Common location for stranded oil following storms. [Module 6 -...Assessment | PowerPoint]
2. Upper Intertidal Zone (UI)
Area immediately below the high tide line.
Inundated during high tides but exposed for much of the tidal cycle. [Module 6 -...Assessment | PowerPoint]
Significance:
Frequently receives stranded oil during tidal fluctuations.
Oil may remain for extended periods between tidal cycles.
Often a priority area for cleanup operations. [Module 6 -...Assessment | PowerPoint]
3. Mid Intertidal Zone (MI)
Middle section of the tidal range.
Regularly exposed and submerged by daily tides. [Module 6 -...Assessment | PowerPoint]
Significance:
Oil is subject to continual reworking by waves and tides.
Natural cleaning processes can be significant.
Oiling conditions can change rapidly between surveys. [Module 6 -...Assessment | PowerPoint]
4. Lower Intertidal Zone (LI)
Lowest part of the intertidal area.
Exposed only during low tide and submerged most of the time.
Significance:
Oil may be mobile and redistributed by waves and currents.
Access for assessment is often limited to low-tide periods.
Timing of surveys is critical for accurate observations.
Why Do We Use Tidal Zones?
Using tidal zones allows SCAT teams to:
Record oiling locations consistently.
Improve accuracy when estimating oil distribution and thickness.
Understand how tides may influence oil movement and persistence.
Develop more effective treatment recommendations.
Monitor cleanup progress and determine endpoint achievement

## Slide 21: Zoning for accurate recording
Image courtesy of OCC
Notes: Show how zoning improves accuracy and consistency when documenting oil distribution.

## Slide 22: Section 6 - Oil Distribution
Use visual aid
% of surface covered by oil in an area
Section 6 - Oil Thickness + Character
Average or dominant oil thickness within the segment or zone
Estimate the actual thickness (cm) of thick / pooled oil and cover
Notes: "Section 6 is often the most important part of the SCAT survey because it quantifies shoreline oiling. We record the percentage of the surface covered by oil, the thickness of the oil, and the physical character of the oil. These observations should be made separately for each shoreline zone and documented using standard SCAT terminology. Consistent recording allows planners and operations staff to compare conditions across segments, prioritize cleanup activities, and track recovery over time.“
Oil Distribution, Cover Estimates, Oil Thickness, and Oil Character
Section 6 of the SCAT form focuses on describing how much oil is present, where it is located, how thick it is, and what it looks like. This is often the most important part of the shoreline assessment because it provides the information needed to develop cleanup recommendations and measure progress. [Module 6 -...Assessment | PowerPoint]
1. Oil Distribution
Oil distribution describes the percentage of the shoreline surface covered by oil within a segment or zone. SCAT teams estimate how much of the ground surface is visibly affected by oil. [Module 6 -...Assessment | PowerPoint]
Key points:
Estimate the proportion of the surface covered by oil.
Record conditions separately for each shoreline zone (A, B, C, etc.).
Use standardized visual aids to improve consistency between teams. [Module 6 -...Assessment | PowerPoint]
Example:
Zone A: 80% oil cover
Zone B: 20% oil cover
Zone C: No visible oil
This provides a much clearer description than assigning a single value to the entire segment. [Module 6 -...Assessment | PowerPoint]
2. Cover Estimates
Cover estimates quantify the amount of oil present on the shoreline surface. The estimate should represent the average or dominant condition within the assessment area. [Module 6 -...Assessment | PowerPoint]
When estimating cover:
Survey the entire zone rather than focusing on isolated patches.
Use agreed SCAT terminology and visual guides.
Record "No Oil" if no oil is observed rather than leaving the field blank. [Module 6 -...Assessment | PowerPoint]
Consistency is critical because treatment priorities are often based on cover estimates. [Module 6 -...Assessment | PowerPoint]
3. Oil Thickness
Oil thickness describes how deep the oil layer is on the shoreline surface. Teams should estimate the dominant or average thickness and note any areas of significantly thicker oil accumulations. Record:
Average or dominant oil thickness within the zone.
Areas of pooled oil separately.
Actual thickness measurements where thick accumulations occur. [
Examples:
Thin film
Stain
Coat
Cover
Thick pooled oil
Thicker oil generally presents a greater environmental risk and may require more aggressive treatment options. [
4. Oil Character
Oil character describes the physical appearance and condition of the oil. Recording oil character helps responders understand weathering, persistence, and likely treatment effectiveness.
Examples include:
Fresh oil
Weathered oil
Tar balls
Asphalt pavement
Thick mousse/emulsion
Oil residue
Surface stain or sheen [The observed character can indicate whether the oil is likely to:
Remain on the shoreline.
Be remobilized by waves.
Respond to natural cleaning processes.
Require active treatment.
Best Practice in SCAT
When recording oiling conditions:
Divide the shoreline into zones. Estimate percentage oil cover. [Record dominant oil thickness. [Describe oil character using standard terminology Support observations with photographs and sketches. Ensure all team members agree on the recorded observations

## Slide 23
Section 7 – Sub-surface oiling
How can oil become buried?
Oil can be buried on shorelines due to wave activity
Influenced by beach substrate and/or storm events
Oil penetrates fine sand beaches less than coarse substrate beaches – less “holes”
Pits and trenches needed to assess if buried oil is suspected
Depth and qualitative description
Notes: "Not all shoreline oiling is visible. Oil can become buried by wave action, storms, and sediment movement, particularly on coarse sand, gravel, and cobble beaches. If buried oil is suspected, SCAT teams may excavate pits or trenches to determine the depth, extent, and character of contamination. This information is critical because buried oil can persist for long periods and may reappear during future storms or shoreline disturbance."
How Does Oil Become Buried?
Several natural processes can cause oil to become trapped beneath the surface:
Wave action: Waves can deposit clean sediment over stranded oil, effectively burying it. [Module 6 -...Assessment | PowerPoint]
Storm events: High-energy events can move large amounts of sand, gravel, or cobbles, covering previously stranded oil. [Module 6 -...Assessment | PowerPoint]
Sediment movement: Natural beach accretion can gradually cover oil deposits over time. [Module 6 -...Assessment | PowerPoint]
Penetration into porous sediments: Oil can migrate downward through gravel and coarse sediments where large pore spaces exist. [Module 6 -...Assessment | PowerPoint]
The depth of penetration is strongly influenced by shoreline type:
Fine sand beaches generally limit oil penetration because there are fewer pore spaces. [Module 6 -...Assessment | PowerPoint]
Coarse sand, gravel, and cobble beaches often allow deeper penetration due to larger void spaces between particles. [Module 6 -...Assessment | PowerPoint]
Why Is Subsurface Oiling Important?
Buried oil can:
Continue to affect shoreline habitats long after surface oil has disappeared. [Module 6 -...Assessment | PowerPoint]
Be remobilized by strong wave action or storms. [Module 6 -...Assessment | PowerPoint]
Contaminate groundwater in some environments. [Module 6 -...Assessment | PowerPoint]
Cause responders to incorrectly assume an area is clean if only surface observations are made. [Module 6 -...Assessment | PowerPoint]
When Are Pits or Trenches Required?
SCAT teams may dig inspection pits or trenches when there is reason to suspect buried oil. [Module 6 -...Assessment | PowerPoint]
Common indicators include:
Historical reports of heavy shoreline oiling. [Module 6 -...Assessment | PowerPoint]
Surface staining or patchy residual oil. [Module 6 -...Assessment | PowerPoint]
Oil sheening when sediments are disturbed. [Module 6 -...Assessment | PowerPoint]
Evidence of recent sediment deposition after storms. [Module 6 -...Assessment | PowerPoint]
Gravel or cobble beaches where deep penetration is likely. [Module 6 -...Assessment | PowerPoint]
Pits and trenches allow teams to:
Determine whether oil is present below the surface. [Module 6 -...Assessment | PowerPoint]
Measure the depth of burial. [Module 6 -...Assessment | PowerPoint]
Estimate the thickness and extent of buried oil. [Module 6 -...Assessment | PowerPoint]
Classify the subsurface oil using SCAT terminology.

## Slide 24
Notes: Review the example and discuss field indicators that suggest buried oil may be present.

## Slide 25: How would you divide the tidal zones to separate the oil distribution % ?
Notes: Ask participants to assess the image and determine appropriate tidal zone divisions.

## Slide 26
A
B
C
D
Notes: Review the proposed zoning solution and discuss the rationale behind each zone boundary.

## Slide 27: Section 7 - Sub Surface Oiling
Notes: Introduce subsurface oiling assessment methods and explain how observations are documented.

## Slide 28
Value | Category | Definition
SAP | Subsurface Asphalt Pavement | Cohesive sediment/weathered oil mixture.
OP | Oil-filled Pares | Pore spaces in the sedirnent matrix filled with oil.
PP | Partially Filled Pores | Pore spaces filled with (oil flows out of sediment when disturbed
OR | Oil Residue | cover 1>0.1 - 1 cm) or Coat(0.01cm ) of oil residue on sediments
OF | oa Film/Stain | Stain (<0.01 Ctn ) or film Oil residue on the sediment surfaces. Non cohesive.
TR | Trace | Discontinuous film or Sport Of Oil on sediments or tackiness with no visible evidence Of Oil
NO | No Oil | No visible or apparent trace of Oill-
Notes: Review the subsurface oiling classification system and explain each category from NO to SAP.

## Slide 29: https://www.youtube.com/watch?v=fr2bfBWiwfA&list=PLuxY5jdD7ksF-SVBS2vM9xY72UI_vrSI4&index=5
Notes: Introduce the supporting video and explain what participants should observe while watching.

## Slide 30: Recap
Write down 3 things learnt from this session
Notes: Summarise the key learning points and ask participants to record three lessons from the session.