## Slide 1
Waste Management & Wildlife Response

## Slide 2: Waste Management & Wildlife Response
List the types of waste generated during oil spill response
1
2
3
Understand the importance of waste management to ensure a smooth response
Understand the risk to wildlife during a response
Objectives
Notes: Understand the importance of planning for waste management prior to an oil spill
Understand the types of waste generated during oil spill response Understand the importance of establishing an efficient waste stream
Understand options for final disposal of wastes
Have a better understanding of wastes types
Understand the importance of waste management to ensure a smooth response

## Slide 3: What waste is generated during an Oil Spill?
List the different types
How can we process this waste?
Notes: Personal Information: Your name, address, contact details, and sometimes your social security number or policy number.
Details of the Incident:
  The date and time of the incident.
  A detailed description of what happened.
  The location of the incident.
Type of Claim: Depending on the nature of the claim (e.g., auto, home, health, travel), the specific questions can vary.
  For auto accidents: details about the other vehicles involved, a police report, and witness information.
  For property damage: the extent of the damage, whether the property was stolen, vandalized, or damaged by natural events.
  For health claims: details of the medical provider, type of injury or illness, and medical reports.
Evidence of Loss:
  Photos or videos of the damage.
  Receipts for any repairs already undertaken or quotes for proposed repairs.
  Medical bills or reports if it's a health-related claim.
Proof of Ownership: In cases of property claims, proof that you own the item(s) claimed for, such as purchase receipts or serial numbers.
Third Party Details: Information about any other parties involved in the incident, including their contact information and insurance details if applicable.
Police Report: For claims involving theft, vandalism, significant property damage, or auto accidents, a copy of the police report may be required.
Witness Information: Names and contact details of any witnesses to the incident.

## Slide 4: Waste Hierarchy
Water
Oil Spill Products
Dead Wildlife
Sediments
Debris

## Slide 5: Waste VS Response Strategy
Response Strategy | Wastes collected & generated
Dispersant application | 
Containment and Recovery | 
Shoreline Cleanup | 
In situ burning | 

## Slide 6: Waste VS Response Strategy
Response Strategy | Wastes collected & generated
Dispersant application | PPE Dispersant drums
Containment and Recovery | Oiled vessels, booms, skimmers Liquid oil / water Emulsified oil PPE
Shoreline Cleanup | Oiled vessels, machinery. beach materials/vegetation, debris, animals Liquid oil / water Emulsified oil PPE
In situ burning | Fire damaged boom Oiled vessels

## Slide 7: What does history tell us ………….casualties
Amoco Cadiz…225K lost
Waste … 85K liquid.. 165K solid
Katina P…1,100K lost
Waste …1,400K liquid…30K solid
Exxon Valdez…35K lost
Waste …13K liquid…33K solid
Haven…140K lost
Waste …9K liquid…28K solid
Braer…85K lost
Waste …0 liquid…2K solid
Sea Empress…72K lost
Waste …22K liquid…12K solid
Erika…20K lost
Waste …1K liquid…250K solid
Deepwater Horizon…932K lost
Waste …120K liquid…1,828K solid

## Slide 8: Waste Volume Consideration
Emulsification
4-5 times volume increase
3750m³
Offshore Recovery
20% - volume decrease
3,000m³
Shoreline Impact
10-20 times volume increase
60,000m³
TOTAL Disposal volume
60,000m³
Evaporation
750m³
25% –volume decrease
Spilt Volume
1000m³

## Slide 9: Waste Hierarchy
Fuel oil spilt in harbour during bunkering options
Notes: 1. Reduce
Reducing waste in the context of an oil spill primarily focuses on minimizing the amount of oil released and thus the waste generated.
- Preventive Measures: Use double-hulled tanks and better quality hoses and connectors to decrease the likelihood of spills.
- Improved Training: Regular and rigorous training for personnel involved in bunkering operations can reduce accidents that result in spills.
- Better Monitoring: Implement real-time monitoring of oil transfer to detect and address leaks immediately.
2. Reuse
Reusing involves finding ways to use the contaminated materials again without processing.
- Oil Booms and Absorbents: Contaminated booms and absorbents can be cleaned and reused in situations where they will still be effective. This is dependent on the type of material and the degree of contamination.
- Contaminated Water: Water used in the clean-up process can be treated and reused for industrial processes or cleaning within the same operation.
3. Recycle
Recycling involves processing the contaminated materials to recover usable products.
- Oil Recovery: Oil recovered from spills, skimmed from water or separated from other debris, can be reprocessed and refined to be used again.
- Recycling Absorbent Materials: Materials designed to absorb oil can sometimes be processed to separate the oil, which can then be recycled. The materials themselves can sometimes be recycled or used as fuel.
4. Recover
Recovery focuses on extracting energy from waste materials.
- Waste-to-Energy: Use incineration to convert heavily contaminated absorbents and other organic materials into energy. This is particularly useful when recycling or cleaning isn't practical or possible.
- Bioremediation: Deploy bioremediation techniques where microorganisms break down or assimilate the oil, effectively converting pollutants into less harmful substances.
5. Landfill
Landfilling should be the last resort, used when the material cannot be treated or processed in any other way that is safe or economical.
- Secure Landfills: Ensure that materials that have to be landfilled are disposed of in facilities designed to handle hazardous waste, preventing leachate from contaminating groundwater and soil.
- Treatment Before Disposal: Treat the waste materials to stabilize and contain the contaminants before sending them to a landfill to minimize environmental impact.
Each step of this hierarchy reduces the environmental impact of waste generated from an oil spill and emphasizes making the most out of unfortunate incidents by maximizing resource efficiency.

## Slide 10: How can we reduce waste?
Fuel oil spilt in harbour during bunkering options
Reducing waste in the context of an oil spill primarily focuses on minimizing the amount of oil released and thus the waste generated.
Preventive Measures: Use double-hulled tanks and better quality hoses and connectors to decrease the likelihood of spills.
Improved Training: Regular and rigorous training for personnel involved in bunkering operations can reduce accidents that result in spills.
Better Monitoring: Implement real-time monitoring of oil transfer to detect and address leaks immediately.

## Slide 11: How can we reduce waste?
Fuel oil spilt in harbour during bunkering options
Reusing involves finding ways to use the contaminated materials again without processing.
Oil Booms and Absorbents: Contaminated booms and absorbents can be cleaned and reused in situations where they will still be effective. This is dependent on the type of material and the degree of contamination.
Contaminated Water: Water used in the clean-up process can be treated and reused for industrial processes or cleaning within the same operation.

## Slide 12: How can we reduce waste?
Fuel oil spilt in harbour during bunkering options
List the final steps in the process for this scenario

## Slide 13: Example: Deep Water Horizon 2010
Initially the clean up was on highly visible areas
Pressure mounted to clean every last drop of oil from public
1000s km of absorbent boom – was tainted with minerals not oil
Inefficient methods being used which could not technically be justified (e..g hair)

## Slide 14: Primary Storage Offshore

## Slide 15: Primary Storage Shoreline

## Slide 16: Primary Storage Shoreline

## Slide 17: Waste Transportation
An efficient method of transportation must be in place to transfer waste from site
Transport must be sealed to be oil-tight
Locally available, suitable transport should be identified in the contingency plan
All vehicles to be kept outside the ‘hot-zone’
Legislative requirements must be met
  hazardous goods labelling
  transport licenses
Notes: Suitable vehicles need to be sourced to transport waste from primary storage to intermediate storage sites.
Must be carried out regularly and efficiently or no further recovery can take place.
Vehicles must be suitable for the terrain.
Any vehicle used must be oil-tight to prevent leakage and secondary contamination of roads and the surrounding area.
Transportation company must meet national legislative requirements for standards etc.

## Slide 18
Transfer out of difficult access sites
Notes: In certain areas the access may be minimal so techniques for disposal may require :
Helicopter, Very expensive and weather dependant.Will require a qualified helicopter marshal.
Aerial rope way, needs to be set up by in a safe manner and not overloaded and protect areas under the line of run from secondary pollution.
Ladder, not recommended for safety reasons.

## Slide 19: Final Disposal - Recycle & Recover
Reprocess the products into a new use.
Recover energy from products.
Use as a fuel in some industrial processes:
  NO debris permitted,
  Need to remove water as the high salt content can corrode pipe work,
  Co-fed with normal crude/fuel feed so very slow,
  Need huge amount of storage to house oil until processed,
  Use in drilling process.

## Slide 20: Direct Disposal
This is the final and arguably most challenging stage of waste management and must take into consideration:
Transport to final site
Disposal options and locality
Approved site
Low oil content
Sandwich the oily waste
Note; very difficult to find sites that will receive oily waste especially a lot !!
Notes: Highlight importance of segregating waste
Whole waste consignment can be classed as waste oil even if only a small part is oiled
Will come back to talk about disposal options at the end of the presentation.

## Slide 21: Gravity Separation
Legacy of the Erika spill - Donges Refinery
Notes: Example of solid washing from the Sea Empress spill using a cement mixer. The contaminated sediment will be added to the mixer with water and possibly a small amount of cleaning agent (eg diesel). This is mixed and a certain amount of the oil will be removed.
Points to note
The sediments must be of relatively small particle size
The waste must be relatively homogenous
The technique will not be effective for heavily contaminated sediments
Ideally sediments, once clean, will be returned to the beach. However, there is often difficulty in deciding when sediment is “ oil free” and so can be returned to the beach.
For larger sediments this technique will no longer be effective. These may be cleaned over a grill. However this is time consuming and produces a great deal of oily water.

## Slide 22: Thermal Treatment
Direct burning.
Portable incineration.
Domestic / industrial incineration.
Other thermal treatment techniques.
Notes: Burning
Direct burning, some countries allow burning at sea
Needs to be controlled
Boom is expensive
Minimum thickness of 6mm for ignition
No good on emulsified oils due to the high water content
Portable incineration
Can be done onsite
Needs a good flow of air to dilute the atmospheric pollution
Often there is legal restrictions preventing its use.
Domestic / industrial incineration
Slow due to the normal day to day domestic waste treatment
Issue of oiled waste containing a high volume of salt causing corrosion to the incinerators.
Approval is required for all options
High temperature industrial incinerators are more able to deal with this kind of waste. However, they are often few and far between and costly.
Alternative Options
Cement factories may take oily waste as a raw material
Pyrolysis: Converts organic oily waste into gas and solid residues through indirect heating without oxygen.
Thermal Desorption: Organic oily wastes are heated to vaporise the contaminants without oxidising them. High organic or moisture content may increase cost and increases the difficulty of treating the gas emissions.

## Slide 23: Stabilisation
Addition of quicklime / binding agent
Easier to transport as less leaching
Renders the oil inert for use in
  Road construction
  Land reclamation
  Landfill
.
Notes: Burning
Direct burning, some countries allow burning at sea
Needs to be controlled
Boom is expensive
Minimum thickness of 6mm for ignition
No good on emulsified oils due to the high water content
Portable incineration
Can be done onsite
Needs a good flow of air to dilute the atmospheric pollution
Often there is legal restrictions preventing its use.
Domestic / industrial incineration
Slow due to the normal day to day domestic waste treatment
Issue of oiled waste containing a high volume of salt causing corrosion to the incinerators.
Approval is required for all options
High temperature industrial incinerators are more able to deal with this kind of waste. However, they are often few and far between and costly.
Alternative Options
Cement factories may take oily waste as a raw material
Pyrolysis: Converts organic oily waste into gas and solid residues through indirect heating without oxygen.
Thermal Desorption: Organic oily wastes are heated to vaporise the contaminants without oxidising them. High organic or moisture content may increase cost and increases the difficulty of treating the gas emissions.

## Slide 24: Bioremediation
Accelerated biodegradation.
Addition of nutrients: bio-enhancement / bio-stimulation.
Addition of micro-organisms: bio-augmentation.
Notes: Bioremediation
Accelerated bio-degradation
Addition of nutrients known as bio-enhancement or enrichment
Nutrients such as composts, fertilisers and lime
Requires constant mixing, aerating and moisture
Addition of manufactured super bugs known as bio-augmenation
This process should ideally be carried out in a controlled environment to prevent the possible destruction of the surrounding unaffected media, but can be done on the shoreline with close monitoring
If it is to be carried out on the shoreline small areas are to be tested initially.
To be carried out at low tide on stranded to prevent the bugs being washed away
Example of bio-augmentation. This photo is taken on Clifton beach, Pakistan after the Tasman Spirit.
May not be necessary to add any bioremediation products – lots of sewage etc on the beach, enough to break down the oil naturally

## Slide 25: Bioremediation Facility Philippines
Separation and sorting area
Treatment area; tilling and moisture addition
Nutrient storage
Final product low ppm
Notes: Burning
Direct burning, some countries allow burning at sea
Needs to be controlled
Boom is expensive
Minimum thickness of 6mm for ignition
No good on emulsified oils due to the high water content
Portable incineration
Can be done onsite
Needs a good flow of air to dilute the atmospheric pollution
Often there is legal restrictions preventing its use.
Domestic / industrial incineration
Slow due to the normal day to day domestic waste treatment
Issue of oiled waste containing a high volume of salt causing corrosion to the incinerators.
Approval is required for all options
High temperature industrial incinerators are more able to deal with this kind of waste. However, they are often few and far between and costly.
Alternative Options
Cement factories may take oily waste as a raw material
Pyrolysis: Converts organic oily waste into gas and solid residues through indirect heating without oxygen.
Thermal Desorption: Organic oily wastes are heated to vaporise the contaminants without oxidising them. High organic or moisture content may increase cost and increases the difficulty of treating the gas emissions.

## Slide 26: Waste Management Planning and Regulation
      Types
      Volumes
      Rate of Generation
      Minimisation
      Segregation
Availability
Location
Capacity
Legislative controls
Availability
Location
Capacity
GENERATION
At Sea and Shore
TEMPORARYSTORAGE
TREATMENT AND / OR DISPOSAL
transport
handling &
transport
handling &
All these factors must be considered in the contingency planning stage:
All factors are influenced by Laws and Regulations…
Notes: All these factors must be considered in the contingency planning stage. It should be treated as a managed project always taking into consideration the Laws and Regulations.

## Slide 27: Oiled Wilidlife

## Slide 28
Click to View

## Slide 29: Wildlife at Risk
Impact: Oil reduces insulation and flight capability, leading to hypothermia and impaired foraging.
Ingestion: Preening birds may ingest oil, causing internal damage and potential death.
Skin and Eye Irritation: Oil causes irritation and potential chemical burns.
Ingestion and Inhalation: Consuming or breathing volatile oil compounds leads to internal poisoning and respiratory issues.
Coating: Oil disrupts physiological functions and contaminates nesting beaches, affecting hatchling survival
Marine Birds
Marine Mammals (whales, dolphins, seals)
Sea Turtles
Where can we find this information?

## Slide 30: Wildlife at Risk
Direct Toxicity: Oil suffocates eggs and larvae; taints adult fish, making them unfit for consumption.
Smothering: Oil blocks breathing or feeding capabilities, causing suffocation.
Reproductive Harm: Oil exposure impairs reproduction, threatening population viability.
Habitat Destruction: Oil destroys crucial habitats like mangroves and marshes.
Food Web Disruption: Contamination affects food sources, leading to starvation and reduced reproduction in dependent species.
Fish
Invertebrates (corals, crabs, shellfish)
Shoreline Fauna

## Slide 31: Oiled Wildlife Response Network
For each country find out:
The name of the response Organisation
What are their areas of expertise?
Click to View

## Slide 32
https://vimeo.com/97120696?fl=pl&fe=cm

## Slide 33: Recap
List three things you have learnt from this session